## Slide 1
Project Presentation of CO-OP Project at Industry (Module-2) (22CS421)
On
Neuromorphic Computing Chips for Low-Power Edge AI Applications
Akshat Khurana | Akshat Gupta | Akshit Mishra
2210991227 | 2210991225 | 2210991239
Supervised By
Dept. of Computer Science Engineering, Chitkara University, Punjab
Department of Computer Science and Engineering,
Chitkara University, Punjab

## Slide 2
Introduction
2
Artificial intelligence (AI) now powers everything from voice assistants to autonomous vehicles
Edge devices (wearables, drones, IoT sensors) must run AI under strict power and latency constraints
Conventional GPUs and CPUs are too power-hungry for many edge deployments
Neuromorphic computing mimics the brain's spiking neural architecture to deliver AI at ultra-low power
This research evaluates neuromorphic chips as a practical solution for low-power edge AI applications

## Slide 3
Problem Statement
3
Modern AI models require up to 400W for training and 10W+ for inference on GPU-class hardware
Edge devices typically operate on batteries with a budget of 1–10 mW
Frame-based CNNs process all pixels every cycle - wasteful when most data is redundant
Existing solutions trade accuracy for efficiency without addressing the fundamental compute paradigm
A fundamentally different hardware-software co-design is needed to bridge the power gap

## Slide 4
Background: From Biological Neurons to Silicon
4
Neurons receive electrical impulses through synapses; membrane potential accumulates until a firing threshold is reached
After firing (action potential / spike), the neuron resets - energy is used ONLY during firing, enabling inherent efficiency
Neuromorphic chips emulate this: each neuron circuit has an internal membrane potential variable that charges with incoming spikes
Leaky Integrate-and-Fire (LIF) model: dv/dt = (I - v) / tau - simplest and most hardware-friendly biological neuron model
LIF neurons reset to zero after firing and are widely implemented in silicon due to low circuit complexity
The human brain runs ~86 billion neurons on less than 20 watts - the gold standard neuromorphic chips aim to approach

## Slide 5
Spiking Neural Network (SNN) Architecture
5
SNNs communicate via discrete spikes - neurons only fire when their membrane potential exceeds a threshold
Leaky Integrate-and-Fire (LIF) model: dv/dt = (I - v) / tau - biological neuron approximation
Event-driven computation: no spike = zero power consumed, unlike always-on CNN activations
STDP (Spike-Timing Dependent Plasticity): on-chip unsupervised learning rule
Asynchronous routing eliminates the clock - reduces idle power to under 1 mW
On-chip SRAM stores synaptic weights locally - avoids costly off-chip memory access

## Slide 6
Literature Review: Intel Loihi
6
Loihi (Davies et al., 2018): first fully digital neuromorphic research chip by Intel, built on 14 nm process technology
128 cores, each simulating 1,024 neurons and synaptic connections - over 128 million potential simulated synapses
Unique programmable on-chip learning engine: implements STDP and custom learning rules without external assistance
Benchmark: energy-delay product more than 5,000x better than conventional CPU on sparse coding tasks
Asynchronous design (no central clock): each core activates only when receiving a spike - granular power control
Loihi 2 (Intel 4 process): up to 1 million neurons, 120 million synapses; NeuEdge framework raised core utilization from 47% to 89%

## Slide 7
Literature Review: IBM TrueNorth
7
TrueNorth (Sawada et al., 2016): 4,096 neural cores manufactured by Samsung on 28 nm CMOS process
256 neurons per core with 256 x 256 synapse grid: 1 million neurons and 256 million synapses on a single chip
Total chip power: only 70 mW - equivalent to a small LED bulb; capable of 6,000 video frames per second
IBM created full software ecosystem: Compass simulator, Corelet programming language (MATLAB), and DNN conversion tools
Researchers train networks in GPU frameworks, then convert to TrueNorth with minimal manual intervention
Real-world validated: handwritten character recognition and weld fault detection at >80% accuracy, far below laptop power draw

## Slide 8
Advanced Frameworks: NeuEdge & NeurEfficient
8
NeuEdge (Imanov et al., 2026): three-component framework deployed on Loihi 2 for edge device neuromorphic AI
Hybrid spike encoding uses both timing and rate of spikes, requiring 4.7x fewer spikes than rate coding alone
Hardware-aware training increases chip core utilization from 47% to 89%, reducing unnecessary inter-core traffic from 41% to 12%
Adaptive threshold mechanism adjusts firing threshold based on noise levels, saving ~67% of power during idle periods
NeuEdge achieves 847 GOPS/W efficiency with 91-96% accuracy across image, gesture, and speech recognition tasks
NeurEfficient (Saini & Gupta, 2025): FPGA + neuromorphic hybrid achieves 87% energy savings on image tasks, 64% on language tasks

## Slide 9
Memristor-Based Neuromorphic Architectures
9
Memristors change resistance based on current flow - electrically analogous to biological synapses that adjust connection strength
Crossbar arrays perform multiply-accumulate operations (core neural network math) directly in memory using analogue physics
Eliminates the von Neumann bottleneck: no costly data transfers between memory and processor units
Achieves total energy efficiency of 75 to 181 TOPS/W (Xia et al., 2025) - among the highest of any platform evaluated
One demonstrated chip powered entirely by a fingernail-sized solar cell, enabling inference in battery-less remote environments
Key challenge: memristor conductance drifts over time when powered off, gradually degrading stored synaptic weights

## Slide 10
Key Neuromorphic Platforms Compared
10
IBM TrueNorth: 1 million neurons, 4,096 cores, 65 nm CMOS, 70 mW - pioneer large-scale chip
Intel Loihi 2: 1 million+ neurons, 128 cores, Intel 4 process, 1 W - supports on-chip learning
BrainScaleS-2: 512 neurons/chip, 65 nm, analog - fastest real-time factor (10,000x biological speed)
NeuEdge (Loihi 2 framework): 847 TOPS/W efficiency - highest in comparison
Memristor Accelerator: 0.01 W, 127 TOPS/W - emerging non-volatile synaptic memory technology
Baseline: NVIDIA Jetson Nano GPU - 10 W, 5 TOPS/W - conventional edge reference

## Slide 11
Table I: Neuromorphic Hardware Platforms Summary
11
Platform | Process Node | Neurons | Power | Main Use
Intel Loihi 2 | 14 nm Intel | 1 million | 250-500 mW | Research, Edge AI
IBM TrueNorth NS1e | 28 nm Samsung | 1 million | 70 mW (chip) | Mobile, IoT
IBM NS16e (4x4) | 28 nm Samsung | 16 million | 7.68 W idle | Scale-up tasks
BrainChip Akida | 28 nm TSMC | 1.2 million | below 1 mW | Always-on IoT
FPGA + CMOS hybrid | Virtex + 28 nm | 128x128 cores | Adjustable | Hybrid research
SpiNNaker (ARM) | 130 nm ARM | 100 million | Variable | Large simulation

## Slide 12
Energy Efficiency Results (Table I)
12
NeuEdge on Loihi 2 achieves 847 TOPS/W - 169x better than Jetson Nano (5 TOPS/W)
Intel Loihi 2 standalone: 60 TOPS/W at only 0.02 W power draw
Memristor accelerator: 127 TOPS/W at 0.01 W - most power-frugal platform tested
Energy savings of 85–95% estimated vs GPU baseline through sparse spike operations
Energy per synaptic op: 0.08 pJ (Loihi) vs 8.6 pJ (GPU) - 107x reduction
Result: neuromorphic platforms are feasible for healthcare wearables (~5 mW budget)

## Slide 13
Table II: Energy Efficiency Comparison
13
Processor / Platform | Power (W) | Efficiency (TOPS/W) | Energy Saved vs. GPU
GPU (Jetson Nano) | 10.0 | 5 | Baseline
Intel Loihi 2 | 0.02 | 60 | 90%
NeuEdge on Loihi 2 | 0.241 | 847 GOp/s/W | 99%
Memristor Accelerator | 0.01 | 75 to 180 | 95%
NeurEfficient Hybrid | 0.005 | above 80 | 87%

## Slide 14
Latency Results (Table II)
14
MobileNet on Jetson Nano (baseline): 18.4 ms per inference
SNN on Loihi 2: 8.9 ms - 52% improvement over CNN baseline
NeuEdge on TrueNorth: 4.1 ms - 78% improvement
NeuEdge on Loihi 2: 2.3 ms - 87% improvement (best result)
Loihi 2 with STDP anomaly detection: 3.0 ms - 75% improvement
Event-driven computation eliminates redundant frame processing - key factor in latency gains

## Slide 15
Table III: Inference Latency Comparison
15
Platform | Task | Latency (ms) | Improvement vs. CNN
MobileNet on Jetson Nano | Image recognition | 18.4 | Baseline
Standard SNN on Loihi 2 | Image classification | 8.9 | 52% faster
NeuEdge on Loihi 2 | Gesture recognition | 2.3 | 87% faster
NeuEdge on TrueNorth | Keyword spotting | 4.1 | 78% faster
Loihi with STDP | Anomaly detection | below 3 | 75% faster

## Slide 16
Accuracy Results (Table III)
16
MobileNetV2 on Jetson Nano: 92.1% accuracy, 62.9 mJ per image.
ANN-to-SNN conversion on Loihi 2: 91.2% accuracy, 5.04 mJ - preserves accuracy with 91% energy saving
NeuEdge on Loihi 2: 92.4% accuracy, 1.21 mJ - best balance of accuracy and efficiency
Direct SNN training: 88.7% accuracy, 3.38 mJ - 3.4% accuracy gap vs DNN, 94% energy saving
TrueNorth NS1e: 89.0% accuracy at only 0.1 mJ - best for ultra-constrained applications
Conclusion: accuracy gaps are narrowing as training methods improve (ANN-to-SNN conversion)

## Slide 17
Table IV: Accuracy and Power on CIFAR-10 Classification
17
Method & Platform | Accuracy (%) | Latency (ms) | Power (mW) | Energy/Image (mJ)
MobileNetV2 on Jetson Nano | 92.1 | 18.4 | 3,420 | 62.9
Quantised DNN on Raspberry Pi | 91.3 | 47.2 | 1,840 | 86.8
Standard SNN on Loihi 2 | 88.7 | 8.9 | 380 | 3.38
ANN to SNN on Loihi 2 | 91.2 | 12.3 | 410 | 5.04
NeuEdge on Loihi 2 | 92.4 | 4.2 | 287 | 1.21
TrueNorth NS1e | approx. 89 | below 1 | 70 | below 0.1

## Slide 18
Table V: Applications of Neuromorphic Edge AI
18
Application Area | Specific Use | Power Budget | Measured Performance
Healthcare wearables | Continuous ECG monitoring | 5 mW | Continuous 24/7 detection
Industrial IoT | Factory motor fault detection | 8 mW | Fault detected below 3 ms
Robotics / UAVs | Obstacle avoidance on micro-drones | 287 mW | 30 frames per second
Smart city sensors | Environmental anomaly detection | 6 mW | 10-year solar-powered life
Manufacturing | Weld defect detection (laser) | ~70 mW | 80% accuracy
Voice assistants | Always-on wake word detection | 67 mW | 82-day coin cell life

## Slide 19
Tools & Technologies Used
19
Brian2: Python-based spiking neural network simulator for LIF neuron scaling experiments
SNNTorch: PyTorch-based SNN library for deep learning-style spiking network training
PyTorch + TorchVision: DNN baseline training and MNIST dataset handling
NumPy + Matplotlib: Numerical analysis and figure generation for all paper charts
Google Colaboratory: Free cloud Python environment with NVIDIA T4 GPU acceleration
MNIST Dataset: 70,000 handwritten digit images used for accuracy and energy benchmarking

## Slide 20
Conclusion
20
Neuromorphic chips deliver 52–87% lower latency and 85–95% lower energy vs GPU baselines
NeuEdge framework on Loihi 2 achieves the best overall performance: 847 TOPS/W, 2.3 ms, 92.4% accuracy
Accuracy gap between SNNs and DNNs has narrowed to ~3% with ANN-to-SNN conversion techniques
Real-world deployments validated: healthcare (5 mW), robotics (287 mW), smart city (6 mW)
Software simulations (Brian2, SNNTorch) corroborate all table data trends and energy estimates
Future work: larger SNN models, on-chip STDP learning, multi-modal sensor fusion at the edge